Mantis completes 953-meter drill program at its Cree Lake Gold Property. Awaits assays.

Toronto, Ontario – August 6, 2009, Mantis Mineral Corp (‘Mantis’-CNSX ‘MYN’) is pleased to announce completion of a 953-meter NQ drill program on its 100% owned Cree Lake gold property where recent trenching and sampling (including 15 to 50cm spot channel sampling and vertical 28-cm long vertical core-plugs of the Flint Rock occurrence yielded gold values as high as 1,300 gpt (37.91 opt.). High grade gold values (greater than 1.0 opt gold) have been reported from 30 of the 122-samples.  Of the 30-samples, 8 yielded assay results greater than 4.0 opt,5 yielded an assay result greater then 2.0 opt while the remainder (17) were over 1.0 opt gold.   The highest grade sample yielded 37.91 opt gold from mineralized quartz-carbonate vein material containing native gold, pyrite and galena. The drill program commenced on July 6th and was completed on July 30th. As of August 1st all of the core samples have been submitted to ALS Chemex for analysis.

A total of seven holes were completed, five of the holes tested the immediate vicinity of the Flint Rock occurrence within a 150-meter strike length. Two holes were drilled beyond this area extending the targeted strike length effectively to 275-meters.

CL09-2 and CL09-5 tested the down dip projection of the vein-structure which on surface carried high grade gold values as above. CL09-2 intersected the zone at a 43-meter vertical depth and encountered a 4.5-meter fault zone hosting several quartz veins containing up to 7% pyrite. CL09-5 drilled along the same section but targeted the vein structure at a 100-meter vertical depth. This hole intersected three zones: an upper 10-meter intersection exhibits silicification, multiple quartz veining with variable pyrite content; a middle section that contains multi-phase quartz veining with variable pyrite and chalcopyrite; and a lower 6-meter intersection containing multi-phase carbonate-quartz veins with variable pyrite content..

Significantly, CL09-6 and 7 were collared 150-meters east of the Flint Rock occurrence and hole CL09-6 intersected veining visually displaying the same traits as the high grade vein 150-meters west. The veining was intersected at 18.5 and 19.8-meters. Pyrite, chalcopyrite and galena were observed which correlate with the high grade surface gold values. Further down the hole at 48-meters, a 3-meter intercept hosts quartz-carbonate veining and silicification with variable pyrite and galena. Other significant intercepts were from 52.85-56.55-meters and 128.07-130.5-meters. CL09-7 undercut hole CL09-6 and intersected a zone from 60.08-71.8-meters of mult-phase quartz carbonate veining and late stockworks veining.

Correlation of all intercepts is pending data compilation and analytical results. In general, visually, the core displays many of the same traits as the high grade Flint Rock vein on surface.  Deformation and veining occur along flow horizons and lithologic contacts. Some of the mineralized quartz veins and silicification halos contain 3-20% pyrite, chalcopyrite and galena within broader meter-scale zones of late carbonate stockworks.

All of the cores were split in half, not exceeding 1-meter sample lengths, respecting lithologies and vein styles. The collected samples were sent to ALS Chemex prep lab in Sudbury. Assay results for these samples are pending. Mantis expects to have all the results by mid September.

A follow-up stripping program in the vicinity of the two most easterly drill holes is being contemplated, pending assay results. A quartz vein, characteristic of the high grade Flint Rock vein sampled last fall was intersected at a shallow depth in one of the eastern holes. This vein should project to sub-crop, where stripping is viable allowing to geologically establish its relationship with the high grade vein situated 150-meters west.

Commented Robin Ross, CEO: “The visual results are encouraging as the veins occur in clusters at depth. Should they contain sufficient grades to form a semi-continuous zone at meter width we could be onto something truly significant. Just as significant are our recent compilation of historical results which have indicated a remarkable number of high grade gold values both at surface and at depth reported by various past operators. This initial drill program should provide a meaningful interpretation of the gold bearing potential of the system.”

This news release has been viewed and approved by Walter Hanych, senior geologist and project manager, who is responsible for program design and quality control of exploration undertaken by the Company.

About Mantis Mineral Corp.

Mantis Mineral Corp. is a Canadian based resource and exploration company traded publicly under the symbol MYN on the CNSX. Mantis is focused on creating shareholder value through the exploration and development of its suite of strategically located, high-impact Canadian exploration projects.

The CNSX has not reviewed and does not accept responsibility for the adequacy of this release.

For further information: Mr. Robin Ross, Chairman & CEO: (416) 362-1800, rross@mantismineralcorp.com, or visit our corporate website at www.mantismineralcorp.com/